## Slide 1
LNTB
Smart Tomato Farming System
IoT + AI-driven irrigation, ripeness detection, and cost tracking for net-house tomato farming in Cambodia
Leading Next-Gen Tomato Business
Laravel · Flutter · Arduino (ESP32)

## Slide 2
THE PROBLEM
Farmers are managing tomato crops on guesswork
1
No moisture visibility
Farmers can't measure soil moisture precisely, leading to over- or under-watering that hurts crop growth.
2
Guesswork harvesting
Ripeness is judged by eye across thousands of plants — inconsistent and labor-heavy.
3
Unknown true cost
Water (m³) and electricity (kWh) usage per day is rarely tracked, making profit hard to calculate.
Location: commercial net-house / cherry tomato farms across Cambodia
2

## Slide 3
PROJECT OBJECTIVES
Three goals driving the system design
01
Smart Irrigation
Design and install smart soil-moisture sensors to auto-control irrigation, plus measure real water (m³) and electricity (kWh) usage.
02
Ripeness Detection
Develop a sensor + AI camera system to evaluate and confirm which fruit has reached harvest-ready standard.
03
Mobile Application
Build a mobile app to log daily operations (irrigation count, water, power) and push real-time notifications to farmers.
3

## Slide 4
SYSTEM ARCHITECTURE
Three layers, one intermediary
IoT / Firmware
ESP32 · ESP32-CAM
Arduino (C++)
Laravel Backend
MySQL · Sanctum
Reverb · FCM
Flutter Mobile App
Riverpod · GoRouter
Khmer UI
HTTPS / JSON →
← REST + WebSocket + FCM
Design principle: firmware and the mobile app never talk directly — Laravel is the single source of truth for data, cost calculation, and notifications.
Sensor → Irrigation Trigger → Cost Calculation → Dashboard + Notification
4

## Slide 5
HARDWARE COMPONENTS
Sensor & control bill of materials
Component | Purpose | Qty | Cost (USD)
ESP32 Microcontroller | Main sensor node controller | 1 | $7.00
ESP32-CAM | Ripeness detection camera | 1 | $12.00
Soil Moisture Sensor | Soil moisture reading | 2 | $4.00
DHT22 | Temperature & humidity | 1 | $4.50
LDR Sensor + Servo Motor | Light + auto net roof | 1 set | $6.00
2-Ch Relay + Pump + Fan | Irrigation / ventilation control | 1 set | $20.00
Wiring & enclosure | Assembly | — | $30.00
Mobile App + Cloud budget | Dev & test server | — | $20.00
Component
Purpose
Qty
Cost
Total Estimated Budget
$103.50
per net house
Budget-conscious sourcing keeps the system affordable for small and medium farmers.
5

## Slide 6
SOFTWARE STACK
One stack per layer
Firmware
• C++ (Arduino Framework)
• PlatformIO / Arduino IDE
• DHT, ESP32Servo, HTTPClient
• ArduinoJson, esp32-camera
Backend
• Laravel
• Sanctum (auth)
• Reverb (realtime)
• MySQL
• Firebase Cloud Messaging
Mobile App
• Flutter
• Riverpod (state)
• GoRouter (routing)
• Dio (HTTP)
• Khmer .arb localization
6

## Slide 7
REQUIREMENTS SUMMARY
39 functional requirements across three modules
13
FR-HW
Firmware
Sensor reads, command polling, pump/servo control, fallback logic, camera capture.
14
FR-BE
Backend
Ingestion, cost calc, broadcasting, notifications, auth, logbook queries.
12
FR-APP
Mobile App
Dashboard, manual control, ripeness view, cost view, logbook, Khmer UI.
Plus 10 non-functional requirements covering usability, performance, reliability, security, and localization.
7

## Slide 8
PROJECT TIMELINE
May – August, four phases
May
Ideation
Team discussion, identify farmer problems, initial proposal, task allocation.
June
Design
Schematic design, net-house prototype, app UI/UX design, hardware procurement.
July
Build & Test
Assemble hardware, write firmware, train AI on ripeness images, install app, field test.
August
Finalize
Refine system from test results, summarize outcomes, final presentation.
8

## Slide 9
Expected Impact
20–30%
Reduction in water & electricity waste via automated shut-off
100%
Ripeness classification clarity — removes guesswork from harvesting
100%
Khmer-language interface — accessible to all skill levels
Sustainability: targeted irrigation conserves groundwater and cuts unnecessary electricity use, aligned with green agriculture practices.
9

## Slide 10
Thank You
LNTB — Leading Next-Gen Tomato Business
Questions & Discussion
10